## Slide 1: Tofino Backend

## Slide 2: Tofino physical pipeline
MAU pipe resources shared between ingress and egress on a fairly fine grain
Multiple parsers (one per port) with separart ingress an egress
Separate ingress and egress deparsers (one of each)
MAU
Parser
Parser
Deparser
Deparser
Ingress
Egress

## Slide 3: Logical Pipeline
Packets run through ingress pipe, then egress pipe
Packets may be replicated between ingress and egress
Parser
MAU
Deparser
Parser
MAU
Deparser
Ingress
Egress

## Slide 4: Tofino Backend IR
Top level IR::Tofino::Pipe class just holds the ingress and egress directly
MAU is a sequence of tables (initially unplaced)
TablePlacement will decide which resources in which stage(s) each table will use
class IR::Tofino::Pipe {
class thread_t {
Tofino::Parser parser = nullptr;
MAU::TableSeq mau = nullptr;
Tofino::Deparser deparser = nullptr;
}
thread_t[2] thread = {}; // INGRESS and EGRESS

## Slide 5: Tofino Parser/Deparser IR
Parser is an unrolled state machine
  Each state has a list of extract/set_metadata primitives and a match to select the next state
Deparser is a list of emit primitives

## Slide 6: Anatomy of a Tofino Table
i
P
H
V
Input
xbar
hash
Match
table
gateway
Match
central
Pred
imem
Action
Data
counter meter selection
VLIW
ALUs
o
P
H
V
Next table
Many components, each of which may or may not be used for any given table
Each part uses resources of some type that are shared between all tables in a stage
Any given table and resource can be allocated to ingress or egress

## Slide 7: Tofino MAU stage
i
P
H
V
Input
xbar
hash
Match
gw
VLIW
ALUs
o
P
H
V
Next table
Match
Central
Attached tables
imem
Match
gw
Match
Central
Attached tables
imem
Match
gw
Match
Central
Attached tables
imem
x16 logical tables
.
.
.

## Slide 8: Table control dependency graph
Table
Sequences of tables that are NOT control dependent
Control dependent tables under next map
Keys are action names or $true, $false, $miss …
Non data-dependent tables in sequence may be reordered
Table Sequence
Table
Table
. . .
Next[action1]
. . .
Next[action2]

## Slide 9
class MAU::Table : Tofino::Unit {
cstring name;
gress_t gress;
int logical_id = -1;
vector<std::pair<Expression, cstring>> gateway_rows;
NullOK ActionFunction gateway_payload;
NullOK IR::V1Table match_table;
inline Vector<Attached> attached;
inline NameMap<ActionFunction, ordered_map> actions;
inline NameMap<TableSeq> next;
// a sequence of tables -- may be reordered if deps allow.
// deps(i,j) is true iff tables[i] is dependent on tables[j]
// (so must have j < i) */
class TableSeq {
inline Vector<Table> tables;
LTBitMatrix deps;

## Slide 10
control ingress {
if (data.b2 == 1) {
apply(test1);
} else {
apply(test2);
}
}
mau: [1050] MAU::TableSeq deps=
[1052] MAU::Table name=cond-0 gress=ingress logical_id=-1
gateway_row: [594] Equ
...
$true: [1056] MAU::TableSeq deps=
[1058] MAU::Table name=test1 gress=ingress logical_id=-1
match_table: [449] V1Table name=test1
[607] ActionFunction name=setb1
...
[63] ActionFunction name=noop
$false: [1062] MAU::TableSeq deps=
[1064] MAU::Table name=test2 gress=ingress logical_id=-1
match_table: [457] V1Table name=test2
[607] ActionFunction name=setb1...
[63] ActionFunction name=noop

## Slide 11: Tofino Backend Passes
A series of transforms lowering the IR to a pattern that matches up with the hardware constraints and requirements.
Try to make the passes independent so they can run in any order, but dependencies do exist.

## Slide 12: Tofino Backend Passes
Metadata management passes
  AddBridgedMetadata
  AddMetadataShims
  CreateThreadLocalInstances
Gateway transforms
  CanonGatewayExpr
  SplitComplexGateways
  CheckGatewayExpr
  SpreadGatewayAcrossSeq
Informational passes
  PhvInfo
  FieldDefUse
  FindDependencyGraph
  TablesMutuallyExclusive
  TableFindSeqDependencies
Table Layout and Placement
  TableLayout
  TablePlacement
  IXBarRealign
Parser/Deparser passes
  ComputeShifts
  SplitExtractEmit
  SplitBigStates
  LoadMatchKeys
PHV Allocation
  PHV::TrivialAlloc
  PhvAllocator
  MauPhvConstraints
  SplitPhvUse
Miscellaneous passes
  CopyHeaderEliminator
  CheckTableNameDuplicate
  DumpPipe
  ElimUnused
  InstructionSelection
Asm Generation
  ParserAsmOutput
  MauAsmOutput
  DeparserAsmOutput

## Slide 13: Informational Passes
PhvInfo
  Collects all the fields and other things in the program that need to be allocated in the PHV
  Place for PHV allocation to store its results
  Helper functions for getting the information (a PhvInfo::Field) related to any IR::Expression
FieldDefUse
  Collects information about all program components that read and write every field
  Helper functions for querying the writes that reach any given read or reads that use any given write
  Conflict matrix recording fields with overlapping live ranges (after table placement)
FindDependencyGraph
  Finds Match/Action/WriteAfterRead dependencies between tables globally
TableFindSeqDependencies
  Find dependencies between tables in a TableSeq (including between control dependent tables)
TablesMutuallyExclusive
  Find table pairs that are mutually exclusive (can never both run on a single packet)

## Slide 14: Metadata management
AddBridgedMetadata
  Adds a fake header deparsed by ingress and parsed by egress to carry metadata from ingress to egress
AddMetadataShims
  Add extra extracts for input metadata for both ingress and egress
CreateThreadLocalInstances
  Ensure all fields have unique names across both ingress and egress

## Slide 15: Gateway Transforms
CanonGatewayExpr
  Transforms gateway expressions into canonical (disjunctive normal) form for easier processing
SplitComplexGateways
  Find gateway expressions that are too complex to fit in a single Tofino gateway block and split them
CheckGatewayExpr
  Check for gateway expressions that are too complex for Tofino and issue error messages
SpreadGatewayAcrossSeq
  Find gateways that control a sequence of tables and duplicate them so each table has its own gateway, rather than all being control dependent on a single gateway (improves table placement possibilities)

## Slide 16: Table Layout and Placement
TableLayout
  Figure out the “shape” of tables – how many xbar groups and width of matches, how to pack action data into overhead or action data tables, how many ways for exact match
TablePlacement
  Pick logical order for tables, reordering non-dependent tables to fit
  Split tables across stages if they’re too big for one stage
  Combine match tables with gateways in a single logical table
  Allocate rams, tcams, and ixbar space for tables
IXBar realign
  Rearrange data in ixbar to meet alignment constraints with respect to PHV use.
  Backtrack to redo Layout and Placement if it fails

## Slide 17: Parser/Deparser related passes
ComputeShifts
  Figure out how much to shift out of input buffer in each parser state and where everything is as a result
SplitExtractEmit
  Split extract and emit primitives to split a single PHV container each
SplitBigStates
  Split states that have too many extracts of a single size
LoadMatchKeys
  Figure out how parser match keys get loaded in a state prior to where they are used

## Slide 18: PHV Allocation
PHV::TrivialAlloc
  Trivial PHV allocator that just allocates every field to its own PHV container of the appropriate size.
  Minimal support for combining containers only when needed for bit/byte alignment in parser/deparser
PhvAllocator
  Ortools based PHV allocator
MauPhvConstraints
  Finds some constraints based on field use in MAU pipe and stores them in the PhvInfo
  Currently unused
SplitPhvUse
  Split operations in the pipeline based on PHV allocation (wide fields split across containers turn into multiple operations)

## Slide 19: Miscellaneous passes
CopyHeaderEliminator
  Turn add/remove/copy_header primitives into a sequence of simple assignments
CheckTableNameDuplicate
  Sanity check
DumpPipe
  Dump the current IR in reasonable compact form if –v flag was used
ElimUnused
  Dead code elimination
  Remove trailing headers that are just parsed and deparsed and never touched in the pipe
InstructionSelection
  Convert primitives into tofino instructions